## Slide 1
領先創新·
·超越自我
2019 Synopsys ARC盃電子設計競賽

## Slide 2: SMART FIREFIGHTER
August 2019
UETer: DANG Hai Ninh & VU Huong Giang
VNU Key Laboratory for Smart Integrated Systems (SISLAB)
VNU University of Engineering and Technology (VNU-UET)
Notes: Hi, I’m Ninh, from Sislab, VN National University. The project I will present today is smart firefighter, a system which can detect location of the fire and spraying water flow to the fire correctly.

## Slide 3: Agenda
Motivation and objectives
Design implementation
Test results
Conclusion
Notes: My presentation includes...

## Slide 4: Agenda
Motivation and objectives
Design implementation
Test results
Conclusion
Notes: The First, my...

## Slide 5: Motivation
NIST, “Dry Scotch Pine Tree Fire”, source: https://www.youtube.com/watch?v=fsaLCdC3iWw
Quick methods to identify and extinguish fire saving lives and properties
8 seconds
16 seconds
4 seconds
1 second
Notes: Look at the pictures, you can see a Christmas tree bursts into flames in less than 7 seconds, and turned into disaster with only 16 seconds, so...

## Slide 6: Motivation (cont.)
Smoke sensor:
Slow detection
No location of flame
Wide water spray nozzle:
Waste water
Causing damage to other furniture
Industrial flame sensor
Sensitive and fast fire detection
No location of flame
Expensive
Fire extinguisher
Heavy
Limited visibility
Traditional methods
Notes: Overview of popular firefighting methods, The most common method is to use a fire extinguisher, but heavy and don’t run when you sleep.

## Slide 7: Our objective: low-cost smart fire fighter
Autonomously detect and extinguish the fire
Quick and accurate detection of flame location
Spraying water flow to the fire correctly, while keeping other areas dry
Fire detection: Low-cost InfraRed Sensors
3D-printed robot arms
ARC EM Starter kit-based algorithms & controls
Notes: So, that is our objective...

## Slide 8: Agenda
Motivation and objectives
Design implementation
Test results
Conclusion
Notes: Now, this is...

## Slide 9: Processing flow
Start
IR camera send pixel array to EMSK
EMSK calculates the distance to the heat source and
determines "IS IT A FIRE?”
YES
The two
axis robot arm sprays water to put out the fire
NO

## Slide 10: System components
2x thermal sensor 32x24 pixel
FOV: 55°x35°
Water pump
2 axis robot arm
2 stepper motor
H bridge
UART
UART
Flame directions
Flame directions
Calculate flame locations
Spray water
Move spray nozzle
ARC EM Starter Kit
Two low-cost Infrared sensors
3D-printed robot arms controlled by step motors
One water pump

## Slide 11: Flame Detection
Flame location: (Fx, Fy, )
calculated from sensor data
Fx and Fy: solved by trigonometric calculation
Hottest pixel: xh = 2, yh = 1
- X angle:  = (55/32)*xh
- Y angle:  = (35/24)*yh
- 2 sensor: 1, 2, 1, 2
Angle calculation from sensors
Detection range: 4m x 4.4m x 4.4m

## Slide 12: 3D-printed robot hand for spraying water
Robot arm 3D model
3D-printed robot arm with two step motors
Extinguish fire by using a robot hand with two joints to spray water to the position of fire

## Slide 13: ARC EM Starter Kit connections
  J3 : 2 Stepper driver module.
  J1 & J5 : 2 IR camera module (using UART).
  J6 : Relay module for water pump control

## Slide 14: Agenda
Motivation and objectives
Design implementation
Test results
Conclusion

## Slide 15: Demonstration setup
Fire: a candle
Robot arm
IR Sensors
ARC EM Starter kit

## Slide 16: Candle flame visualization using a single sensor
Distance: 1m
Distance: 2m
Distance: 3m
Notes: At 1 meter, The candle shows 103c,...

## Slide 17: Agenda
Motivation and objectives
Design implementation
Test results
Conclusion

## Slide 18: Conclusions
Fire grows very fast in home environment & Industrial smart firefighters are very expensive
Our proposal: Low-cost Smart Fire Fighter
  Low-cost IR sensor for fire detection
  3D-Printed Robot arm for water control for extinguishing fire
  Using ARC EM Starter Kit for algorithm development & control
Future works
  Multi-sensor nodes with wireless connections
  Embedded machine learning for fire classification
Notes: In future, We have plans setup Multi-sensor nodes with wireless connections to Extend protection area.